## Slide 1
ELEG2310B
Tutorial 5
Pulse Modulation, Review and Exercises
Teaching Assistants: WANG, Runbang; TIAN, Feng
runbang@link.cuhk.edu.hk
Notes: Tutorial 5: Pulse Modulation. Teaching Assistants: WANG, Runbang; TIAN, Feng. runbang@link.cuhk.edu.hk. Source: Fall2026/Note7_PAM.pdf, pp. 1.

## Slide 2
Modulation
Transmission
Demodulation
Ideal channel

## Slide 4
AM schemes
PM
FM
PAM
Sinusoidal carrier
Change amplitude
Change phase
Change frequency
Pulses
Change pulse height

## Slide 5
Pulse modulation
PAM
Modulation
Demodulation
One sample: change height, width, or position
PAM: the sample value sets the pulse height.
Notes: The pulse replaces the sinusoid as the signal shape. Compare the response to one changing sample: height for PAM, width for PDM, and time position for PPM. Only PAM is developed here. Source: Fall2026/Note7_PAM.pdf, pp. 2-4.

## Slide 6
PAM
Take samples, then form pulses
Continue
Notes: Show all three actual objects: the message, its impulse samples, and the pulse shape h. Sampling comes first; a selected weighted impulse then shifts/scales one h, after which linear addition makes the complete s. Same five-sample finite-sinc example as page6; negative sample n=2 has value -0.5. No quantization. No time-domain multiplication by h. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t).

## Slide 7
PAM
Derivation: Pulse construction
Continue
Optional derivation of the preceding result.
Notes: Optional adjacent derivation of the result just stated; not a further signal-processing stage. The target is the already-seen pulse signal. Show why convolving the impulse samples with h produces those pulses. Keep the defining integral, substitution, sum exchange and sifting before the dominant final signal. Source: Fall2026/Note7_PAM.pdf, pp.10. Teaching revision: explain the local operation before mathematics. Time-domain examples use the same exact finite sinc sum with samples 0.5,1,-0.5,0.8,-0.3 at n=0..4, all other integer samples zero. Spectral-copy illustrations separately use the explicitly announced triangular spectrum. No quantization; ideal noiseless, synchronized receiver.

## Slide 8
PAM
Derivation: The sampling clock
Continue
Optional derivation of the preceding result.
Notes: Optional proof part1. Retain Note7 Fourier-series reasoning and coefficient integral over one period. Write the impulse train explicitly instead of adding delta_Ts notation. This calculation justifies the clock-transform result already given. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t).

## Slide 9
PAM
Sampling repeats the message spectrum
Continue
Notes: Continue from the established frequency convolution. Reuse the impulse-convolution shift already explained in time. Animate one shifted triangular M first, then add the other copies. Explicit diagram normalization Ts removes only the common scale; W=fs/3 is an announced spectrum illustration, not the earlier finite-sinc message. Full Note7 Fourier-series calculation follows immediately as an optional proof. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t).

## Slide 10
PAM
Nyquist Sampling Theorem
Notes: Sampling can preserve all message information only if the spectral copies stay apart. Keep the same bandlimited message while changing fs. Compare W and fs-W, derive the source Nyquist condition, and state the boundary-tone restriction beside it. Source: Fall2026/Note7_PAM.pdf, pp.8. Teaching revision: explain the local operation before mathematics. Time-domain examples use the same exact finite sinc sum with samples 0.5,1,-0.5,0.8,-0.3 at n=0..4, all other integer samples zero. Spectral-copy illustrations separately use the explicitly announced triangular spectrum. No quantization; ideal noiseless, synchronized receiver.

## Slide 11
PAM
Derivation: The pulse response
Continue
Optional derivation of the preceding result.
Notes: Optional adjacent derivation of the result just stated; not a further signal-processing stage. The sampling analysis located spectral copies. Now isolate the second operation: forming a finite rectangular pulse. Find H from the same h; retain integral, exponential factor, sine identity and sinc definition. This page supplies the multiplier used next. Source: Fall2026/Note7_PAM.pdf, pp.11. Teaching revision: explain the local operation before mathematics. Time-domain examples use the same exact finite sinc sum with samples 0.5,1,-0.5,0.8,-0.3 at n=0..4, all other integer samples zero. Spectral-copy illustrations separately use the explicitly announced triangular spectrum. No quantization; ideal noiseless, synchronized receiver.

## Slide 12
PAM
S(f): combine the two known factors
Notes: The time and frequency expressions describe the same transmitted signal: s=m_delta*h and S=M_delta H. Sampling determines M_delta; pulse shape determines H. Substitute each established factor back into S. Bandwidth is a property of S, not an extra transmission stage. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t). Conditions: 0<T<Ts; bandlimited messages; fs>=2W with no boundary tones at equality. The pulse first-null scale 1/T is not strict support.

## Slide 13
PAM
Read each flat pulse at its centre
Notes: The received flat-top pulse heights give the original sample values. Read the heights first, then reconstruct from the complete impulse sample stream using Ts times an ideal LPF. The sinc interpolation is the time representation of that same reconstruction. The time example uses the same five nonzero samples throughout; the separately announced triangular spectrum illustrates the frequency calculation. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t). Conditions: 0<T<Ts; bandlimited messages; fs>=2W with no boundary tones at equality. The pulse first-null scale 1/T is not strict support.

## Slide 14
PAM
Recover the message spectrum
Notes: Source: Fall2026/Note7_PAM.pdf pp.14-17. Fourier convention exp(-j2 pi f t). Unit LPF cutoff fs/2; fs=1/Ts, fs>=2W, no boundary tones at equality. Reconstruct after reading the flat pulse heights. Triangle spectrum is a general nonaliasing frequency illustration, distinct from the finite sinc time example. The known ideal filter kernel avoids explicitly transforming the sample stream and the filtered spectrum in a symbolic solution; no claim about universal numerical complexity.

## Slide 15
PAM
Shift, weight, then add the sinc responses
Notes: Source: Fall2026/Note7_PAM.pdf pp.14-17. The selected time-domain reconstruction is m=Ts hLP*m_delta. The scaled kernel Ts hLP=sinc(t/Ts), with fs Ts=1. Keep the same finite example: Ts normalized to1, five nonzero samples [0.5,1,-0.5,0.8,-0.3], all other integer samples zero; m is their exact finite sinc sum, not a claim that arbitrary messages require only five samples. A unit sinc is shifted to each nTs, weighted by m(nTs), then the responses are added. The marked sinc centre (nTs,m(nTs)) corresponds to the marked input sample; negative coefficients invert the curve. Reconstruction passes every integer sample. No new G, g, or frequency detour.

## Slide 16
PAM
Derivation: the reconstruction response
Continue
Notes: The received flat-top pulse heights give the original sample values. Read the heights first, then reconstruct from the complete impulse sample stream using Ts times an ideal LPF. The sinc interpolation is the time representation of that same reconstruction. The time example uses the same five nonzero samples throughout; the separately announced triangular spectrum illustrates the frequency calculation. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t). Conditions: 0<T<Ts; bandlimited messages; fs>=2W with no boundary tones at equality. The pulse first-null scale 1/T is not strict support.

## Slide 17
PAM
Derivation: add the weighted responses
Continue
Notes: The received flat-top pulse heights give the original sample values. Read the heights first, then reconstruct from the complete impulse sample stream using Ts times an ideal LPF. The sinc interpolation is the time representation of that same reconstruction. The time example uses the same five nonzero samples throughout; the separately announced triangular spectrum illustrates the frequency calculation. Source: Fall2026/Note7_PAM.pdf pp.5-17. Fourier convention exp(-j2 pi f t). Conditions: 0<T<Ts; bandlimited messages; fs>=2W with no boundary tones at equality. The pulse first-null scale 1/T is not strict support.

## Slide 18
TDM
Multiplexing
Modulation
Demodulation
Commutator: interleave three sample streams
Notes: Use the same pulse heights for multiple messages. The commutator takes one sample from each of three messages during each interval Ts, placing them in successive time slots. A message is still sampled every Ts; the common stream has three times as many pulses. In this sequential illustration the actual sampling times are t_(n,i)=nTs+(i-1)Ts/3, not simultaneous samples from all channels. Input messages are bandlimited with fs>=2W. Source: Fall2026/Note7_PAM.pdf, pp. 18-19.

## Slide 19
TDM
Demultiplexing
Modulation
Demodulation
Decommutator: separate the time slots
Same clock and slot assignment; reconstruct each message.
Notes: The decommutator uses the same slot assignment and timing clock to direct each pulse to the right message stream. Each stream then uses the same reconstruction filter, with its own known sample-time offset. The formula is the previous interpolation formula translated to the sample times t_(n,i). Timing synchronization is required; otherwise pulse heights can be assigned to the wrong channel. These ideal demonstrations omit transmission distortion and noise. Source: Fall2026/Note7_PAM.pdf, pp. 19.

## Slide 20
PAM and TDM
Takeaways
Modulation
Demodulation
Bandlimited messages; no boundary tones at equality.
Task | Operation | Result
Generate PAM | Sample, then form pulses | Sample value = pulse height
Avoid aliasing | Separate spectral copies | 
Recover m | Read heights, then reconstruct | Weighted sinc pulses add to m
Share the channel | Interleave time slots | Synchronized TDM
Notes: Return to the four outcomes of the same pulse-message path. Pulse height stores a sample; sampling creates copies which must remain separated; a reconstruction filter combines shifted sinc pulses to recover the message; TDM interleaves and separates several sample streams using synchronized slots. Conditions: strictly bandlimited messages, the sampling-theorem endpoint assumptions, isolated pulses with 0<T<Ts, and an ideal channel. Source: Fall2026/Note7_PAM.pdf, pp. 5-19.

## Slide 21
End of Tutorial 5
Questions?
For the animated slides, please email
runbang@link.cuhk.edu.hk
Notes: For the animated slides, contact runbang@link.cuhk.edu.hk. Source: Fall2026/Note7_PAM.pdf, pp. 1.

## Slide 22
Review
Transmitted signals
Practice
AM
DSB-SC
SSB
QAM
PM
FM
PAM
Multiplexing
FDM
Add frequency bands
TDM
Interleave slots

## Slide 23
Review
AM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: AM: The envelope follows the message. Example: message 1 Hz; carrier 8 Hz; modulation depth 0.6. Source: Note3 pp.4-8,10-12. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 24
Review
DSB-SC - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: DSB-SC: Multiply the message by the carrier; retain its sign. Example: message 1 Hz; carrier 8 Hz; local oscillator amplitude 2. Source: Note4 pp.3-9. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 25
Review
SSB - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: SSB: Keep one sideband and its negative-frequency mirror. Example: keep the USB lines at +9 and -9 Hz; each weight is 0.25. Source: Note4 pp.11-15. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 26
Review
QAM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: QAM: Use cosine and sine at the SAME carrier frequency. Example: two messages at 1 and 2 Hz; one carrier at 12 Hz. Source: Note4 pp.16-21. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 27
Review
PM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: PM: Add a phase proportional to the message. Example: message 1 Hz; carrier 8 Hz; phase sensitivity 1.2. Source: Note6 pp.2-4,9,12-15; approved TTR4 PM-recovery/Carson recap. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 28
Review
FM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: FM: Set frequency deviation proportional to the message. Example: message 1 Hz; carrier 8 Hz; peak frequency deviation 1.5 Hz. Source: Note6 pp.5,9,16-19,23-27. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 29
Review
PAM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: PAM: Sample the message; use each value as a pulse height. Example: sample rate 8/s; pulse width 0.07 s; message 1 Hz. Source: Note7 pp.5-16. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 30
Review
FDM - The complete process
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Recover
Generate
s(t) / S(f)
Notes: FDM: Modulate separately, then add nonoverlapping frequency bands. Example: three 2-Hz allocations; two 2-Hz guards; total span 10 Hz. Source: Note5 pp.3-8. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 31
Review
TDM - The complete process
Generate
Time slots
Recover
Generate
Time slots
Recover
Generate
Time slots
Notes: TDM: Interleave sample streams into synchronized time slots. Example: each message 4 samples/s; three messages share 12 pulses/s. Source: Note7 pp.18-19. Ideal noiseless matched receiver. Reconstruction gains and assumptions are stated beside the corresponding result.

## Slide 32
Practice
Questions and reference solutions
18 exercises
Signals and Systems
Exercises 1 - 5
AM and DSB-SC
Exercises 6 - 8
SSB and QAM
Exercises 9 - 11
FDM and Frequency Translation
Exercises 12
PM and FM
Exercises 13 - 15
PAM and Sampling
Exercises 16 - 18
Back to s(t)

## Slide 33
Practice
Exercise 1: Fourier Transform by Direct Integration (1/3)
Practice index
Question
Find the Fourier transform of the following signal using direct integration, and sketch its magnitude spectrum. T > 0 is the window
duration; A is real.

## Slide 34
Practice
Exercise 1: Fourier Transform by Direct Integration (2/3)
Practice index
Solution
Integrate only over the nonzero window and write the cosine as two complex exponentials.
For each shifted frequency a, the integration limits produce a sine divided by its argument. At a = 0 use the continuous limit.

## Slide 35
Practice
Exercise 1: Fourier Transform by Direct Integration (3/3)
Practice index
The sketch is even, has dominant lobes near +/-5/T and nonzero sidelobes extending indefinitely. X(0) = 0 and X(+/-5/T) = AT/2. In the
normalized coordinate u = fT, every integer except +/-5 is a zero. The two signed sinc functions must be added before taking the
magnitude; adding their separate magnitudes is incorrect. The marked value at u = +/-5 is not a claim that the exact global maxima occur
there.
Endpoint note: the printed signal assigns zero at +/-T/2. Any different rectangle convention at these isolated points leaves this Fourier
integral unchanged.

## Slide 36
Practice
Exercise 2: Fourier Pairs and Properties
Practice index
Question
Re-compute the Fourier transform of x(t) in Exercise 1, this time using Fourier-transform pairs and properties rather than direct
integration. The complete signal is repeated here for independent use.
Solution
Represent the signal as a rectangular window multiplied by a cosine whose frequency is 5/T.
Multiplication in time is convolution in frequency. Convolution with each impulse shifts the complete sinc function, including its sign.
This agrees with the direct-integration result.

## Slide 37
Practice
Exercise 3: Triangle, Self-Convolution and Spectrum (1/2)
Practice index
Question
Consider the following signal.
(a) Sketch x(t). Show that it is the self-convolution of a rectangular signal with T = 1 and A = 1. (b) Find X(f) and sketch the magnitude
spectrum |X(f)|.
Solution
(a) x(t) is a triangle of height 1 at t = 0, falling linearly to zero at t = +/-1. Let r(t) = rect(t), a unit-height rectangle supported on [-1/2,1/2].
The product equals 1 precisely on the overlap of the intervals [-1/2,1/2] and [t-1/2,t+1/2]. Its integral is that overlap length.

## Slide 38
Practice
Exercise 3: Triangle, Self-Convolution and Spectrum (2/2)
Practice index
At t = +/-1 the intervals meet at one point and the integral is zero; at t = 0 their overlap length is 1. Rectangle endpoint conventions
therefore do not change the result.
(b) The Fourier transform of rect(t) is sinc(f). The convolution theorem turns the self-convolution into a product.
The spectrum is real, even and nonnegative. Its central lobe lies between f = -1 and 1; smaller lobes extend indefinitely, so the exact
support is not bandlimited.

## Slide 39
Practice
Exercise 4: Rectangular Input to an LTI System (1/2)
Practice index
Question
An LTI system has impulse response h(t) = sinc(t). The input is x(t) = rect(t). Sketch the spectrum of the system output, Y(f). Use sinc(t) =
sin(pi t)/(pi t).
Solution
Convolution with h(t) in time corresponds to multiplication by H(f) in frequency.

## Slide 40
Practice
Exercise 4: Rectangular Input to an LTI System (2/2)
Practice index
Keep the central portion of the sinc only, between -1/2 and 1/2. Y(0) = 1 and its inside-edge limit is sinc(1/2) = 2/pi. The output is not a
rectangle: the passband truncates the sinc without flattening it. Values exactly at the two discontinuities depend on the rectangle convention
and do not affect the inverse Fourier integral.

## Slide 41
Practice
Exercise 5: 3 dB Bandwidth (1/2)
Practice index
Question
Given the following spectrum, where fs = 100 Hz is a given frequency parameter, find its 3 dB bandwidth. Here fs is not a sampling
frequency.
Solution
The course uses the positive, one-sided half-power frequency for the baseband 3 dB bandwidth. Half power means an amplitude ratio
1/sqrt(2), not 1/2.

## Slide 42
Practice
Exercise 5: 3 dB Bandwidth (2/2)
Practice index
The half-power point has amplitude 1/sqrt(2) at 64.36 Hz. An amplitude of 0.5 at 100 Hz instead corresponds to -6.02 dB. The two-sided
half-power interval is [-64.36,64.36] Hz; its width is 128.72 Hz, while the one-sided baseband bandwidth is 64.36 Hz.

## Slide 43
Practice
Exercise 6: AM of a Sinc Message (1/2)
Practice index
Question
Suppose m(t) = sinc(t). Transmit it using conventional AM with carrier c(t) = 2 cos(2 pi fc t), where fc = 40 kHz. (a) Find and sketch M(f).
(b) Sketch the spectrum S(f) of the AM signal. (c) Specify the bandwidths of M(f) and S(f), considering their dominant frequency
components.
First give the spectrum for general k_a. For the numerical spectrum sketch, take k_a = 1.
Solution
(a) Apply duality to rect(t) <-> sinc(f); rect is even.
M(f) has level 1 for -0.5 < f < 0.5 Hz and is zero outside. Thus the exact one-sided baseband support is W = 0.5 Hz.
(b) Separate the unmodulated carrier and the message-bearing product. The factor 2 in c(t) cancels the 1/2 in the cosine transform.

## Slide 44
Practice
Exercise 6: AM of a Sinc Message (2/2)
Practice index
The two rectangles have level 1 and width 1 Hz, centered at +/-40 kHz. Each carrier impulse has weight 1. The positive-frequency band is
[39999.5,40000.5] Hz and the negative-frequency band is [-40000.5,-39999.5] Hz. Impulse weights are not finite ordinary spectral heights.
(c) For the nonzero modulation ka = 1, the baseband bandwidth is the largest positive message frequency; the passband transmission
bandwidth is the width of the positive-frequency band.
Do not call the distance from the far negative-frequency edge to the far positive-frequency edge the transmission bandwidth. The sinc
message is exactly bandlimited, so these are exact support widths. A sufficient envelope condition is |ka| <= 1 because |sinc(t)| <= 1.

## Slide 45
Practice
Exercise 7: DSB-SC Mod-Demodulation (1/3)
Practice index
Question
Let m(t) = sinc(t). Transmit it by DSB-SC using c(t) = 2 cos(2 pi fc t), fc = 40 kHz. The channel is ideal.
(a) Write down s(t). (b) Find and sketch S(f), and specify the transmission bandwidth. (c) For coherent detection, the local oscillator is
c-tilde(t) = cos(2 pi fc t). Derive the product-modulator output v(t). What LPF cutoff recovers the message?
Solution
(a) Multiply the message by the specified carrier, retaining its amplitude 2.
(b) M(f) = rect(f). Each shifted copy has coefficient 1, because the amplitude 2 cancels the cosine's transform coefficient 1/2.

## Slide 46
Practice
Exercise 7: DSB-SC Mod-Demodulation (2/3)
Practice index
There is no carrier-only impulse. The positive band runs from 39999.5 to 40000.5 Hz; its mirrored negative band is required because s(t) is
real.
(c) Use 2 cos^2(theta) = 1 + cos(2 theta). The local oscillator amplitude here is 1, not 2.

## Slide 47
Practice
Exercise 7: DSB-SC Mod-Demodulation (3/3)
Practice index
The baseband rectangle has level 1 and support [-0.5,0.5] Hz. The unwanted rectangles have level 1/2, centered at +/-80 kHz; their nearest
edges are at +/-79999.5 Hz. Choose a unity-gain ideal LPF that passes the full baseband and rejects both images.
No extra recovery gain is needed: the transmitter amplitude 2 and LO amplitude 1 give baseband gain 2 x 1 / 2 = 1. Strict cutoff inequalities
leave a guard gap. An ideal cutoff placed exactly at an ordinary spectral edge can differ only at isolated points under different endpoint
conventions; the strict choice avoids that ambiguity.

## Slide 48
Practice
Exercise 8: Envelope detection of DSB-SC (1/2)
Practice index
Question
A DSB-SC signal is s(t)=A_c m(t) cos(2 pi f_c t), with a baseband message varying slowly compared with the carrier. The two schematic
messages and their transmitted waveforms are shown below; their peak magnitude is denoted M (not numerically specified).

## Slide 49
Practice
Exercise 8: Envelope detection of DSB-SC (2/2)
Practice index
(a) Find the envelope-detector output for m_1(t). (b) Find the output for m_2(t). (c) Explain why envelope detection cannot generally
recover a DSB-SC message.
Solution
(a) The envelope is the nonnegative magnitude of the carrier coefficient. A_c is taken positive.
Thus the negative triangular lobe on 2<t<4 is reflected above the time axis. Dividing by A_c gives |m_1|, not m_1.
(b) The second message is nonnegative and equals |m_1|, so
Dividing by A_c recovers this particular nonnegative m_2. The two different transmitted waveforms nevertheless have identical envelopes.
Envelope detection loses the sign (a pi carrier-phase reversal). For a message bandlimited to |f|<=W with f_c>W and a matched LO, ideal
coherent detection gives:
the finite triangular sketches are schematic slow envelopes, not literally strictly bandlimited waveforms. Their role is to demonstrate sign
loss, not assign a spectral cutoff.

## Slide 50
Practice
Exercise 9: SSB Demodulation Example (1/3)
Practice index
Question
For the given received SSB spectrum, determine the spectrum after matched-carrier multiplication and low-pass filtering, and express the
recovered M(f).
Let U(f) be a triangular lobe on [0,W], with peak a at W/2, and f_c > W. The received positive lobe lies above +f_c and its real-signal
mirror lies below -f_c.

## Slide 51
Practice
Exercise 9: SSB Demodulation Example (2/3)
Practice index
Use an LO 2 cos(2 pi f_c t), whose spectral impulses at +/-f_c have unit weight. The given spectral lobes are real and nonnegative.
Solution
1. The matched 2 cos LO shifts the complete received spectrum both left and right by fc, with unit coefficients.
2. Substitute the two received lobes. Two copies meet at baseband; the other two lie near +/-2fc.
The wanted supports are [0,W] and [-W,0]. The image supports are [2fc,2fc+W] and [-2fc-W,-2fc]. Every lobe keeps its peak a under this
LO normalization.

## Slide 52
Practice
Exercise 9: SSB Demodulation Example (3/3)
Practice index
3. A unity-gain ideal low-pass filter keeps the baseband pair and removes the two images. A cutoff in the open gap is a valid robust choice.
4. The recovered spectrum has the same two triangular baseband lobes, the same peak a, and one-sided bandwidth W. With an LO cos
instead of 2 cos, all of V(f) would be halved and a final gain 2 would be required.
The mixer impulses describe frequency shifts; they are not additional carrier lines in V(f). A magnitude spectrum alone does not specify
the spectral phase of an arbitrary signal.

## Slide 53
Practice
Exercise 10: Three-tone message: Fourier transform and upper-sideband spectrum (1/3)
Practice index
Question
Let 0<f_1<f_2<f_3, with f_i much smaller than f_c. Derive the Fourier transform of the following message, then sketch the magnitude
spectrum when its upper sideband is selected for SSB-SC transmission.
Form m(t) cos(2 pi f_c t), then apply a unity-gain USB bandpass filter. Use no additional amplitude normalization.
Solution
The cosine transform pair gives a pair of impulse lines for every tone:

## Slide 54
Practice
Exercise 10: Three-tone message: Fourier transform and upper-sideband spectrum (2/3)
Practice index
Multiplying by the unit-amplitude carrier makes two shifted copies, each scaled by one half:
The USB filter keeps f_c+f_i and its negative-frequency conjugate mirror -(f_c+f_i), discarding the inner pairs f_c-f_i and -(f_c-f_i):

## Slide 55
Practice
Exercise 10: Three-tone message: Fourier transform and upper-sideband spectrum (3/3)
Practice index
The figure gives line locations; each line has the coefficient stated beside its row. Magnitude-spectrum line weights are |A_i|/2 in M and
|A_i|/4 in the modulated spectra. If all A_i are positive, these equal the signed coefficients. Keeping both frequency signs is necessary for a
real transmitted waveform.

## Slide 56
Practice
Exercise 11: Recovering the sine branch of a QAM signal (1/2)
Practice index
Question
Two messages m_1,m_2 are bandlimited to |f|<=W, with f_c>W. The QAM transmitter and sine-branch mixer share the same nonzero
amplitude A_c:
(i) Express v_2 as a multiple of m_2 plus high-frequency terms. (ii) Fourier-transform this expression and verify the sine-branch spectrum.
(iii) Specify an appropriate LPF cutoff and the gain needed to recover m_2 exactly.
Solution
(i) Expand the product and use cos x sin x=(1/2)sin(2x), sin^2 x=(1/2)[1-cos(2x)]:

## Slide 57
Practice
Exercise 11: Recovering the sine branch of a QAM signal (2/2)
Practice index
(ii) Apply the modulation transform pairs separately to the sine and cosine terms:
The desired term occupies [-W,W]. The unwanted copies occupy bands centered at +/-2f_c, whose nearest edges to zero are +/- (2f_c-W).
The plus-sine transmitter convention produces the positive M_2 baseband term and the minus cosine-image terms shown above.
(iii) Choose a unity-passband LPF with cutoff F_L satisfying
The cutoff can equal W if endpoint content is passed appropriately. Matched carrier frequency and phase are assumed. The LPF output has
gain A_c^2/2; multiplying by 2/A_c^2 recovers m_2 exactly.

## Slide 58
Practice
Exercise 12: How many 10 kHz clients fit in a 20 MHz channel?
Practice index
Question
A service provider has the positive-frequency allocation 800-820 MHz (20 MHz total). Each client has a 10 kHz message. Find the
maximum simultaneous client count for (i) DSB-SC, (ii) SSB-SC, and (iii) QAM. Assume ideal adjacent allocation with no guard bands; a
QAM channel carries two independent clients.
Solution
(i) DSB-SC requires twice the message bandwidth for one client:
(ii) SSB-SC needs one message bandwidth per client:
(iii) One QAM carrier uses 2W=20 kHz but serves two clients, one on each quadrature:
Thus the respective client counts are 1000, 2000 and 2000. Count positive-frequency channel allocation once; its negative-frequency mirror
is not a second usable 20 MHz allocation. A guard-band requirement would reduce these ideal counts; none is assumed here.

## Slide 59
Practice
Exercise 13: The same waveform viewed as PM and FM (1/4)
Practice index
Question
The plotted message is zero outside [0,6], and is linear between (0,2 pi), (2,-2 pi), (4,2 pi), (6,-2 pi). Let A_c=1 and f_c=5 Hz.
(a) Write m_1(t) and its PM signal for k_p=1. (b) Regard that same signal as FM with k_f=1; derive its instantaneous frequency and sketch
its equivalent message m_2(t). (c) Sketch the FM waveform s_FM(t) according to m_2(t).
Solution
(a) Read each line segment from the graph:

## Slide 60
Practice
Exercise 13: The same waveform viewed as PM and FM (2/4)
Practice index
(b) On the open segments, differentiate the total phase and divide by 2 pi:

## Slide 61
Practice
Exercise 13: The same waveform viewed as PM and FM (3/4)
Practice index
Boundary qualification: the displayed m_1 jumps by +2 pi at 0 and 6. Such jumps leave the cosine unchanged. Use a continuous unwrapped
phase for instantaneous frequency; differentiating the discontinuous written phase literally would instead introduce delta impulses. A
suitable unwrapped extra phase is
Its derivative has the ordinary segment values above, without those artificial phase-wrap impulses. Frequency at the segment boundaries
themselves is not assigned.
(c) Substitute the three linear phases; the constant phase offsets are integer multiples of 2 pi:

## Slide 62
Practice
Exercise 13: The same waveform viewed as PM and FM (4/4)
Practice index
There are 8 cycles on [0,2], 12 on [2,4] and 8 on [4,6], with amplitude one throughout. Equivalent PM/FM descriptions use the appropriate
message transformation and phase reference, not the same message inserted into both modulators.

## Slide 63
Practice
Exercise 14: Carson bandwidth estimates (1/2)
Practice index
Question
For f_c=1 MHz, find the transmission bandwidth in each case. The FM sensitivity in (a),(b) is k_f=1000. Use normalized sinc(x)=sin(pi
x)/(pi x).
(a) FM with m(t)=sinc(2t/T), T=0.001 s. (b) FM with m(t)=rect(t/(2T)), T=5x10^-5 s. (c) PM with m(t)=4 pi sin(2 pi f_0 t), f_0=10 kHz,
k_p=1. Finally, discuss whether these cases show FM to be more bandwidth-efficient than AM schemes.
Solution
Carson's rule estimates occupied bandwidth; it is not a statement of finite spectral support. For a bandlimited FM message, use B_T
approximately 2(Delta f+W), with Delta f=|k_f|max|m|.
(a) The transform of sinc(2t/T) is a rectangle supported on |f|<1/T:
(b) For the stated unit-height rectangular message,
Its sinc spectrum has nonzero tails at arbitrarily large |f|, so the message has no finite strict W. A strict-bandwidth Carson calculation is
therefore unavailable. If the explicitly chosen approximation is to take the message's first-null width as an effective W, then

## Slide 64
Practice
Exercise 14: Carson bandwidth estimates (2/2)
Practice index
(c) A PM signal has frequency deviation proportional to the derivative of its message:
Comparison: for the same bandlimited message, AM/DSB occupy 2W and SSB occupies W. Carson gives 2(W+Delta f), so these examples
provide no bandwidth saving for FM. In (a), 4 kHz exceeds the AM/DSB 2 kHz; in (c), the occupied estimate is about 271.3 kHz versus an
AM/DSB width of 20 kHz for that message. Part (b) cannot support a strict-bandwidth comparison without an additional
effective-bandwidth convention. The conclusion concerns bandwidth only, not noise performance.

## Slide 65
Practice
Exercise 15: Selecting RC for an approximate frequency discriminator (1/2)
Practice index
Question
The received FM signal has f_c=400 Hz, k_f=10 and message m(t)=4 cos(2 pi f_0 t), f_0=10 Hz. Choose a suitable RC product for an RC
frequency discriminator. Use the question's stipulated practical criterion 3|2 pi f RC|<1 for the approximation |2 pi f RC| much smaller than
one.
Solution
First find the peak frequency deviation and Carson occupied bandwidth:
The upper positive-frequency edge of that occupied band, rather than the full width added to f_c, is

## Slide 66
Practice
Exercise 15: Selecting RC for an approximate frequency discriminator (2/2)
Practice index
Make the RC approximation valid up to that frequency:
One suitable choice is RC=10^-4 s (for example R=10 kOhm and C=10 nF):
The circuit response is H_RC(f)=j2 pi f RC/(1+j2 pi f RC), approximately RC times an ideal differentiator in the chosen band. Its known
RC gain must be removed if recovering calibrated message amplitudes. Also f_i=400+40 cos(20 pi t)>0, so the differentiated envelope does
not fold in this example.
450 Hz is an estimated occupied-band edge, not a strict maximum FM spectral frequency; small tails remain beyond Carson's band. The
factor-three criterion is the specified engineering tolerance, not an exact mathematical equivalence to 'much smaller'.

## Slide 67
Practice
Exercise 16: Nyquist rates and sampled spectra: sinc versus a boundary sine (1/3)
Practice index
Question
For each message below, determine its bandwidth and nominal Nyquist rate, then sketch the magnitude spectrum after ideal impulse
sampling. Include the cases above, at and below the nominal rate. Samples are taken at t=nT_s with zero time offset.
Solution
For ideal impulse sampling, form and sum the signed/complex spectral copies before taking magnitude:
(a) The sinc transform is a rectangle:
Each replicated rectangle has width 1000 Hz and height f_s T. At f_s=1500 Hz they are separated; at 1000 Hz their edges touch (no impulse
energy at the edges); at 750 Hz they overlap and alias. The following plots show the actual summed magnitude, not independent unadded
copies:

## Slide 68
Practice
Exercise 16: Nyquist rates and sampled spectra: sinc versus a boundary sine (2/3)
Practice index
At f_s=1000 Hz, m(nT_s)=sinc(n) is zero except at n=0, so m_delta(t)=delta(t) and M_delta(f)=1. This edge-touching example remains
reconstructible by an ideal LPF of gain T_s.
(b) The sine has spectral lines at +/-f_0:

## Slide 69
Practice
Exercise 16: Nyquist rates and sampled spectra: sinc versus a boundary sine (3/3)
Practice index
For a nondegenerate illustration choose f_s=30 kHz>20 kHz. Then M_delta has lines at k f_s +/-10 kHz, with magnitude weight f_s/2 each.
At exactly f_s=20 kHz, however,
At that rate, opposite signed/imaginary contributions coincide and cancel; one must not add their magnitudes. Thus the nominal Nyquist
rate is 20 kHz but a phase-independent sampling guarantee for this boundary tone needs f_s>20 kHz.
For a below-rate illustration f_s=15 kHz, m(nT_s)=sin(4 pi n/3)=-sin(2 pi n/3), indistinguishable from a negative 5 kHz sine sampled at
that rate.

## Slide 70
Practice
Exercise 17: PAM of a sinc message at its nominal Nyquist rate (1/3)
Practice index
Question
Let m(t)=2 sinc(4t/T_0), with T_0>0, and use a causal unit-height rectangular pulse h(t)=1 for 0<=t<T and zero otherwise.
(a) Sketch m(t) and derive its Fourier transform. (b) Determine its Nyquist rate, sample at that rate, and sketch m_delta(t) and its
magnitude spectrum. (c) Choose a suitable T and sketch the magnitude spectra of h(t) and the PAM signal s(t). (d) Determine the
transmission bandwidth under the course's first-positive-null convention.
Solution
(a) Scale the normalized sinc transform pair:
(b) The nominal Nyquist rate and its sample interval are

## Slide 71
Practice
Exercise 17: PAM of a sinc message at its nominal Nyquist rate (2/3)
Practice index
All rectangles in f_s sum_k M(f-k f_s) touch edge-to-edge and give the constant 2. This is a finite-energy sinc message without boundary
spectral impulses; it does not share the exact-Nyquist sine cancellation problem. The ideal sampled time sketch is the single impulse of
weight 2 at t=0, with all other sample weights zero.
(c) Choose T=T_s/2=T_0/8, so T<T_s. Convolution with the pulse gives

## Slide 72
Practice
Exercise 17: PAM of a sinc message at its nominal Nyquist rate (3/3)
Practice index
The time-domain PAM output is one rectangle of height 2 over 0<=t<T_0/8. The magnitude spectra share zeros f=+/-8n/T_0 and have
nonzero sidelobes.
(d) The first positive zero is
This is the course's one-sided first-null transmission-bandwidth convention. Rectangular pulses have infinite strict spectral support, so their
spectrum does not stop at 8/T_0.

## Slide 73
Practice
Exercise 18: Sampling rate for a sinusoidal message family
Practice index
Question
For the message family below, determine the smallest nominal sampling rate that covers every allowed message frequency.
Solution
The largest possible message frequency, not its amplitude or carrier phase, sets the band edge:
The nominal Nyquist rate is 400 samples/s. Because the family includes every phase at f_m=200 Hz, equality does not guarantee recovery:
To guarantee preservation of the entire family independently of phase, choose f_s>400 samples/s, for example 500 samples/s. There is no
smallest real-valued rate strictly greater than 400; 400 is the infimum.