## Slide 1
ELEG2310B
Tutorial 5
Pulse Modulation
Teaching Assistants: WANG, Runbang; TIAN, Feng
runbang@link.cuhk.edu.hk
Notes: Tutorial 5: Pulse Modulation. Teaching Assistants: WANG, Runbang; TIAN, Feng. runbang@link.cuhk.edu.hk. Source: Fall2026/Note7_PAM.pdf, pp. 1.

## Slide 2
Modulation
Transmission
Demodulation
Ideal channel

## Slide 4
AM schemes
PM
FM
PAM
Sinusoidal carrier
Change amplitude
Change phase
Change frequency
Pulses
Change pulse height

## Slide 5
Pulse modulation
PAM
Modulation
Demodulation
One sample: change height, width, or position
PAM: the sample value sets the pulse height.
Notes: The pulse replaces the sinusoid as the signal shape. Compare the response to one changing sample: height for PAM, width for PDM, and time position for PPM. Only PAM is developed here. Source: Fall2026/Note7_PAM.pdf, pp. 2-4.

## Slide 6
PAM
Modulation
Modulation
Demodulation
Notes: Take a value every Ts seconds. Represent the sample as a weighted ideal impulse, then replace each impulse by the unit-height pulse h(t). The signal s(t) remains continuous-time. All three plots use the same sample values, including their signs. T<Ts makes the pulses distinct. Source: Fall2026/Note7_PAM.pdf, pp. 5-6.

## Slide 7
PAM
Modulation
Modulation
Demodulation
Convolve with h(t)
Notes: Derive the same pulse signal from the convolution m_delta*h. Substitute the complete impulse sum into the convolution, exchange the sum and integral, and use the delta sifting property. Only the pulse at each sample time survives. This establishes the preceding visual construction without a new signal model. Source: Fall2026/Note7_PAM.pdf, pp. 10.

## Slide 8
PAM
Sampling
Modulation
Demodulation
Locate the frequency copies of the samples.
Notes: The periodic impulse train has a Fourier series. On the centered period only the impulse at zero contributes to the coefficient integral. Thus every Fourier-series coefficient is 1/Ts. The complex exponentials are used solely to locate frequency copies of the same sampled signal. Source: Fall2026/Note7_PAM.pdf, pp. 6-7.

## Slide 9
PAM
Sampling
Modulation
Demodulation
One shifted copy per k; triangular M(f) illustration.
Sampling creates copies spaced by fs.
Notes: Multiply the established impulse-train Fourier series by m(t), then take its Fourier transform term by term. Each modulation by exp(j2pi*k*fs*t) shifts M to k*fs. The animation copies the same spectrum to those centers. Spectral heights in the illustration are normalized by the common factor 1/Ts. Source: Fall2026/Note7_PAM.pdf, pp. 7-9.

## Slide 10
PAM
Sampling
Modulation
Demodulation
Notes: Keep the same strictly bandlimited message while changing fs. Each copy has edges k*fs-W and k*fs+W. Adjacent supports do not overlap when W<=fs-W, yielding fs>=2W as in Note 7. Equality requires the usual treatment of spectral endpoints; the illustrated safely separated case uses fs>2W. Arbitrary tones at the Nyquist boundary need additional qualifications. Source: Fall2026/Note7_PAM.pdf, pp. 8.

## Slide 11
PAM
Pulse shape
Bandwidth of s(t)
Modulation
Demodulation
Notes: Transform the same causal rectangular pulse used to form s. Integrate exp(-j2pi*f*t) over 0<t<T, factor out exp(-j*pi*f*T), and use the sine identity. sinc(x)=sin(pi*x)/(pi*x). Keep the phase factor; the plot displays magnitude only, normalized by T. H(0)=T by continuity. Source: Fall2026/Note7_PAM.pdf, pp. 11.

## Slide 12
PAM
Bandwidth
Bandwidth of s(t)
Modulation
Demodulation
Pulse response H: first positive zero at 1/T.
Notes: Use s=m_delta*h, so S=M_delta H. The magnitude of each repeated spectrum is shaped by the magnitude of the same rectangular-pulse response. The figure uses fs=3W and T=1/(4W), and normalizes the common gains. The pulse spectrum has nonzero tails. Note 7 uses BT=1/T as the first-positive-null bandwidth convention; it is not strict spectral support, nor the full two-sided first-null span. With T<Ts and fs>=2W, this measure is at least 2W. Source: Fall2026/Note7_PAM.pdf, pp. 12-14.

## Slide 13
PAM
Demodulation
Modulation
Demodulation
Notes: Start with the transmitted flat-top pulses s(t), not an already-known message. Read each isolated pulse inside its flat region, for example at nTs+T/2. Its height equals m(nTs). Use these values to form the ideal sampled signal m_delta, to which the lecture reconstruction filter applies. Directly lowpass-filtering s would retain the pulse response H and is not the reconstruction route taught here. Source: Fall2026/Note7_PAM.pdf, pp. 14.

## Slide 14
PAM
Reconstruction
Modulation
Demodulation
Notes: Under the same bandwidth and sampling assumptions, the ideal unity-gain lowpass with cutoff fs/2 passes only the central copy. Its output is m/Ts, so the separate gain Ts restores m. The complete filter response including that gain would be Ts*H_LP. This is the receiver route from the preceding sampled pulse heights. Source: Fall2026/Note7_PAM.pdf, pp. 15.

## Slide 15
PAM
Reconstruction
Modulation
Demodulation
Notes: Return to the same H_LP rectangle. Its inverse Fourier transform is h_LP(t). Evaluate the integral over -fs/2 to fs/2, combine the two exponentials using the sine identity, and identify fs*sinc(fs*t). The animation draws this impulse response and marks its zeros at integer nonzero multiples of Ts. Values at t=0 follow by continuity. Source: Fall2026/Note7_PAM.pdf, pp. 15.

## Slide 16
PAM
Reconstruction
Modulation
Demodulation
Notes: Derive interpolation from the already established reconstruction system. Substitute the ideal impulse sample sum, exchange sum and integral, sift the impulse, substitute h_LP=fs*sinc(fs*t), and cancel Ts*fs=1. Every operation is retained. The result is the same g=m from the preceding frequency-domain argument, not a new reconstruction method. Source: Fall2026/Note7_PAM.pdf, pp. 16.

## Slide 17
PAM
Reconstruction
Modulation
Demodulation
Example: five nonzero samples
Notes: Animate the established interpolation sum: each sample scales and shifts one sinc, and their sum is the reconstructed message. For a finite, exact demonstration the example has five nonzero samples at n=-2,-1,0,1,2, with values 0.5,1,-0.5,0.8,-0.3; all other integer samples are zero. This defines a valid bandlimited example as the displayed finite sinc sum. The light curve is its full sum, the black curve the current partial sum. The general formula remains infinite. At each sample instant its own sinc equals one and every other sinc equals zero, so the value is preserved. Source: Fall2026/Note7_PAM.pdf, pp. 16-17.

## Slide 18
TDM
Multiplexing
Modulation
Demodulation
Commutator: interleave three sample streams
Notes: Use the same pulse heights for multiple messages. The commutator takes one sample from each of three messages during each interval Ts, placing them in successive time slots. A message is still sampled every Ts; the common stream has three times as many pulses. In this sequential illustration the actual sampling times are t_(n,i)=nTs+(i-1)Ts/3, not simultaneous samples from all channels. Input messages are bandlimited with fs>=2W. Source: Fall2026/Note7_PAM.pdf, pp. 18-19.

## Slide 19
TDM
Demultiplexing
Modulation
Demodulation
Decommutator: separate the time slots
Same clock and slot assignment; reconstruct each message.
Notes: The decommutator uses the same slot assignment and timing clock to direct each pulse to the right message stream. Each stream then uses the same reconstruction filter, with its own known sample-time offset. The formula is the previous interpolation formula translated to the sample times t_(n,i). Timing synchronization is required; otherwise pulse heights can be assigned to the wrong channel. These ideal demonstrations omit transmission distortion and noise. Source: Fall2026/Note7_PAM.pdf, pp. 19.

## Slide 20
PAM and TDM
Takeaways
Modulation
Demodulation
Bandlimited messages; no boundary tones at equality.
Task | Operation | Result
Generate PAM | Sample, then form pulses | Sample value = pulse height
Avoid aliasing | Separate spectral copies | 
Recover m | Read heights, then reconstruct | Weighted sinc pulses add to m
Share the channel | Interleave time slots | Synchronized TDM
Notes: Return to the four outcomes of the same pulse-message path. Pulse height stores a sample; sampling creates copies which must remain separated; a reconstruction filter combines shifted sinc pulses to recover the message; TDM interleaves and separates several sample streams using synchronized slots. Conditions: strictly bandlimited messages, the sampling-theorem endpoint assumptions, isolated pulses with 0<T<Ts, and an ideal channel. Source: Fall2026/Note7_PAM.pdf, pp. 5-19.

## Slide 21
Modulation
Review
Modulation
Demodulation
Method | The message controls
AM | Sinusoid amplitude
PM | Added phase
FM | Instantaneous frequency
PAM | Pulse height
FDM: share frequency. TDM: share time.
Notes: Briefly locate PAM alongside the sinusoidal methods already studied. AM changes amplitude, PM adds message-dependent phase, FM puts the message into instantaneous frequency, and PAM puts samples into pulse heights. FDM shares frequency bands; TDM shares time slots. These are multiplexing choices and are not extra alternatives in the carrier-parameter list. Source for earlier methods: Fall2026/Notes 3-6. Source: Fall2026/Note7_PAM.pdf, pp. 2.

## Slide 22
Communication system
TRANSMITTER
CHANNEL
RECEIVER
PCM
Digital PAM
Bandpass modulation
h: distortion / ISI
n: noise
Decode / reconstruct
Detect symbols
Demodulate
Notes: The user-approved closing picture previews the later course: the transmitter may include PCM, digital PAM and bandpass modulation; the channel r=h*s+n can introduce distortion/ISI and noise; matching receiver operations decode, detect or demodulate and reconstruct. These are topic locations, not three obligatory consecutive transmitter stages. PCM and digital modulation are not derived in this tutorial. Source: Fall2026/Note7_PAM.pdf, pp. 2.

## Slide 23
End of Tutorial 5
Questions?
For the animated slides, please email
runbang@link.cuhk.edu.hk
Notes: For the animated slides, contact runbang@link.cuhk.edu.hk. Source: Fall2026/Note7_PAM.pdf, pp. 1.